## Slide 1
Smart Orthotics
Group 16
Ali Saeed
Usman Ali
Gordon Lam
Tony Marissen
Jeff Gorchynski

## Slide 2
Current Pedorthotic Solutions are expensive and do not actively adjust to changes in improper gait.
Review of Problem
$500/2yrs
Useless upon Weight or Gait change
  Design a long-lasting system to economically correct improper gait by actively manipulating the pressure distribution and orientation of the foot that is comfortable and easy to use.

## Slide 3: Design Areas We managed to identify some VERY important areas in our design
Precision measurements of areas that vary
Heel is key to foot orientation, needs high actuation
Arches (both longitudinal and lateral) for gait and posture

## Slide 4
Long lasting
  at least 2 year lifespan
Same price/cheaper than typical orthotics
  $500 or less
Dynamic adjustment of pressure distribution and orientation
  responds within a minute
Comfortable
  Does not strain the foot any more than a regular shoe
User-friendly
  Intuitive and easy to use (learning operation takes <5 min)
Modified Objectives

## Slide 5
Must last at least 2 years
Must cost the same as typical orthotics ($500) or less
Must respond to changes in gait within a minute
Must not strain the foot any more than a regular shoe
Learning its operation must not take more than 5 minutes
Modified Constraints

## Slide 6
Concept Designs
Miniature
Motorized
ScrewJacks
Tiny screwjacks line the underneath of the sole. Pressure points are manipulated by adjusting screw heights
Memory Foam Insole
Heat coils deform the memory foam – sinking the foot at desired locations to correct foot orientation
Air Bubble-wrap Insole
Air bubbles are spread over the entire area of the insole. Foot posture is modified by deflating/inflating key bubbles
Air Muscles
Air muscles are connected to both ends of an elastic insole. When air is pumped, they contract & bend the insole in desired shape

## Slide 7
 | Cost | Weight | Durability | Response Time | Safety/Ergonomics | Aesthetics | Total
 | [Cdn $] | [Kg] | [Yrs of use] | [Sec] | [Hrs of use] | [Size] | 
Weight | 0.3 | 0.1 | 0.3 | 0.1 | 0.1 | 0.1 | 1
Memory Foam | 1 | 1 | 4 | 2 | 1 | 2 | 1.9
Screw-Jack Nail-bed | 3 | 2 | 1 | 2 | 1 | 2 | 1.7
Hydroven FPR | 5 | 5 | 3 | 5 | 1 | 5 | 3.5
Shape-memory Alloy | 2 | 4 | 2 | 4 | 1 | 2 | 1.9
Electro-Active Polymers | 7 | 1 | 2 | 3 | 1 | 2 | 3.1
Decision Matrix

## Slide 8
Preferred Design
Modified Screw-Jack Design
A flexible insole is bent at desired angles when threaded rods push at it. Motors located in the adjustment platform connect to these rods through holes in the bottom of the shoe.
insole
Threaded rods

## Slide 9
Design Breakdown
Material
Sensing
Actuation
Controller
motors
insole
shoe

## Slide 10
Insole
Elastic rubber sheet that morphs when pressure is applied from the threaded rods beneath
Material: ½” rubber sheet
Insole attached to the shoe at perimeter

## Slide 11
Requirements
  Understand the orientation of the foot, how to correct for proper gait
Solutions
  Force sensors
  Strain gauge
Sensing

## Slide 12
Multiple small sensors
At least 8
  4 around the heel
  4 around lateral arch
Measure areas of high variability
Larger sensors at the heel
Analog output
Force Sensing
Size Range = 0.2” x 0.2” – 20” x 24”
Device thickness: 0.20 to 1.25 mm
Force Sensitivity Range: 100 g to 10 kg
Pressure Sensitivity Range: 1.5psi to 150psi
Interlink Electronics 0.2” Circular FSR

## Slide 13
Provides general, qualitative measurements' about shape of foot
Measure arch curvature
  Provides direct feedback for arch-actuation
Analog output
Flex Sensing

## Slide 14
Threaded Rods
Location of threaded rods beneath the sole
Location | Rods
Heel | 3
Arch | 2
Metatarsals | 1
Proximal Phalanges | 1
Inch Thread Size | 5/16"-18
Overall Length | 1-1/4"
Minimum Tensile Strength | 42,000 psi
Part Number: 93225A914

## Slide 15
Motors
Voltage: 12vdc RPM: 263 Torque: 2527oz.in (181.96 Kg-cm) Reduction: 64:1 Shaft length: 55mm 36mm Gearbox
Banebots 12V 263RPM 2527oz-in Planetary Gearmotor w/RS-540 Motor
All motors are installed in the adjustment platform with their shafts revealed. Allen keys are attached to the end of the shafts with a spring that constantly pushes on the threaded rods.
Allen key
Spring
Motor
Threaded Rods

## Slide 16
Proximal Phalange Sliding Arc
To distribute the force beneath the front arch, a sliding arc mechanism is used. When thread rises, the arc opens up, otherwise it closes to change the effective height.
The two pieces of the arch are free to move to conform to the foot while the screw controls the height.

## Slide 17
Controller
dsPIC33FJ128GP802 µC
  40MIPS, 128kB program mem, 16kB RAM
  19 available I/O, 16 re-mapable pins
  2x UART, 2x SPI, 1x I2C
  10x ADC’s @ (1.1msps 10-bit) or (500ksps 12-bit)
  4x DAC’s @ 100ksps, 16-bit
External ADC will link to µC via SPI bus
External motor controller for DC-motor control via DAC or (if more than 4) UART

## Slide 18
Force & Stretch
Sensors
Motor Controller
ADC
Accelerometer
Controller Layout

## Slide 19
Bill of Materials

## Slide 20
Timeline

## Slide 21: Manufacturing/Commissioning
Most manufacturing for the platform will be done in the Student Machine shop
Sensors and Controller implementation will be done in Church Lab
We have allowed for a 2 week test period before we can finalize/commission the design

## Slide 22: Mass Production
Manufacturing will be outsourced to save costs
Injection moulding will be used for metal replacements in the shoe to reduce cost
Bulk purchasing for Electronic components will reduce cost
Prototype Cost | Mass Production Cost
$1000 | $500

## Slide 23: ADJUSTABLE SHOE ARCH SUPPORT
Date of Issue: Sep 8, 1942
Inventors: H.Skorepa Assignees: Preventive Medical Technologies, Inc.
Similarities-differences: Our screw is vertically placed - screw moves vertically to produce vertical arch movement - The net effect is the same - adjustable arch radius of curvature
Description: Screw is longitudinally aligned to foot - translates horizontal screw movement to vertical arch movement.

## Slide 24: VARIABLY ADJUSTABLE SHOE INSERTS
Date of Issue: Apr 16, 1985
Inventors: Dennis N. Brown Assignees: Preventive Medical Technologies, Inc.
Description: The insert (one piece) adapts to the foot to maintain foot orientation. Length is adjustable, but no minor adjustments possible.
Similarities-differences:
Our system has many small adjustment points using screws.

## Slide 25: ADJUSTABLE ARCH, CUSHION INSOLE FOR A SHOE
Date of Issue: March 28, 1995
Inventors: Skinner et. all. Assignees: Preventive Medical Technologies, Inc.
Description:
A static system, with only one adjustment point - the location of the arch. Arch shapes must be varied by using different arch pieces.
Similarities-differences:
Our system has adjustable arch shape and multiple adjustment points.

## Slide 26: ADJUSTABLE ARCH SUPPORT FOR A SHOE
Date of Issue: Jun 6, 1972
Inventors: William M. Matteson Assignees: Preventive Medical Technologies, Inc.
Description: Uses screw to push up on arch via pressure distribution plate. Requires manual screw adjustment.
Similarities-differences: Our arch uses a two-leaf bridge in which the two leaves slide inside each other laterally to create variable height. The actuation in our design is a motorized screw with feedback control.

## Slide 27: Patentable Items
Motorized actuation at multiple points
Two leaf bridge for adjustable arch support
Strain gauge sensors at key points to determine resulting pressure distribution – allows for adjustment and feedback control

## Slide 28
Summary and Questions
Problem Review
  Design a long-lasting economically correct improper gait by actively manipulating the pressure distribution and orientation of the foot that is comfortable and easy to use.
Conceptual Designs
  Miniature Motorized Screw Jacks
  Air Muscles
  Memory Foam Insole
  Air Bubble-wrap Insole
Design Details
  Rubber Insole
  Force, Strain Sensors and Controller
  Two Leaf Arch Support
  Miniaturized Screw Jack
Design Details
  Rubber Insole
  Force, Strain Sensors and Controller
  Two Leaf Arch Support
  Miniaturized Screw Jack
Manufacturing and Commissioning
  Prototype made in University
  Mass Manufacturing with cheaper materials to reduce cost
Patents
  Adjustable Shoe Arch
  Variable Adjustable
  Cushion Insole
  Support for a Shoe
  Patentable Aspects